## Slide 1: Principles of communications Chapter 3 Channel—Part II Channel Capacity 信道容量

## Slide 2
Twisted pairs
Coaxial cable
Optical Fiber
Ground wave
Short Wave
Satellite (LOS)
Chapter 3: Channel — Part II

## Slide 3: Channel bandwidth B and Information rate Rb
Channel bandwidth B is a key parameter in communication systems, describing the ability of a communication channel to transmit signals or data.
Channel | B (Bandwidth) | Rb​ (bps)
Wifi | Depends on standard (e.g., ~20 - 160 MHz for Wi-Fi 6) | Up to ~9.6 Gbps (Wi-Fi 7)
      Information rate Rb：
      the average information content transmitted in unit time, the unit is b/s or bps.

## Slide 4: Discussion
Channel | B (Bandwidth) | Rb​ (bps)
Twisted pairs |  | 
Coaxial cable |  | 
Optical Fiber |  | 
Ground wave |  | 
Short Wave |  | 
Satellite (LOS) |  | 
Wifi |  | 

## Slide 5
Channel | B (Bandwidth) | Rb​ (bps)
Twisted pairs | ~100/250 MHz | ~1 Gbps
Coaxial cable | ~1 GHz | ~10 Gbps
Optical Fiber | ~THz | ~100 Gbps
Ground wave | ~kHz~MHz | ~Mbps
Short Wave | ~MHz | ~tens kbps
Satellite (LOS) | ~500 MHz~GHz | ~100 Mbps
Wifi | ~20–160 MHz | ~9.6 Gbps
Bandwidth is limited by the transmission medium.
Transmission rate has an upper limit called channel capacity.
Maximum

## Slide 6
高速公路最大容量(车辆)
光缆的最大容量 (信息量)
Channel Capacity:信道容量
How to compute the channel capacity of a communication system？

## Slide 7
A Mathematical Theory of Communication，
The Bell System Technical Journal, 1948
Fifty Years of Shannon Theory，IEEE 1998
天才简史——香农
Channel Capacity:信道容量
Shannon theorem 香农定理

## Slide 8
Definition
Discrete Channel Capacity 离散信道容量
Continous Channel Capacity 连续信道容量
Examples
Extension 扩展
Channel Capacity:信道容量

## Slide 9
Definition
Channel capacity: For a given channel, it is the maximum average information‑transmission rate that can be transmitted error‑free, representing an inherent limiting parameter of the channel itself.(对于给定信道，信道能够无差错传输的最大平均信息速率，是信道本身固有的极限参数。)
Channel Capacity:信道容量

## Slide 10
Definition
Discrete Channel Capacity 离散信道容量
Continous Channel Capacity 连续信道容量
Examples
Extension 扩展
Channel Capacity:信道容量

## Slide 11
Discrete Channel capacity:离散
P(1 / 0)
P(0 / 1)
0
0
1
1
P(0 / 0)
P(1 / 1)
Transmitter
Receiver
H(x)
H(y)
H(x/y)
Channel Capacity:信道容量
Channel

## Slide 12
Discrete Channel capacity:离散
P(1 / 0)
P(0 / 1)
0
0
1
1
P(0 / 0)
P(1 / 1)
Transmitter
Receiver
H(x)
H(y)
H(x/y)
Channel Capacity:信道容量
Channel

## Slide 13
Discrete Channel capacity:离散
Channel Capacity:信道容量

## Slide 14
Discrete Channel capacity——example

## Slide 15
Mutual information
Nyquist rate
K=2BT
Unit time is K/T
Gaussian
distribution
—Hartley Y1928
—Shannon Y1948
Shannon-Hartley theorem 香农-哈特利定理
Channel Capacity:信道容量

## Slide 16
    Where S － average transmitted power（W）
    N－ noise power（W）
    B－channel bandwidth（Hz）
For a continuous additive white Gaussian noise (AWGN) channel, the channel capacity is:
Shannon-Hartley theorem 香农-哈特利定理
Channel Capacity:信道容量
What is the difference
between discrete and continuous channel capacity?

## Slide 17
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
--Coding channel model（编码信道模型）
Channel encoder
Channel decoder
Source encoder
Source decoder
Modulator
Demodulator
channel
Source of information
User of information
Encryption
Decryption
Noise
Modulation channel
Coding channel

## Slide 18
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
--Coding channel model（编码信道模型）
Channel encoder
Channel decoder
Modulator
Demodulator
channel
Noise
Modulation channel
Coding channel
The modulation channel is a real physical channel,
while the coding channel is merely an abstract model with statistical properties.

## Slide 19
Discrete Channel Capacity 离散信道容量
离散信道模型：高层抽象
用转移概率表征物理介质带来的差错。
Continous Channel Capacity 连续信道容量
连续 AWGN 信道模型：底层物理视角
直接使用带宽、功率、噪声功率这些物理介质参数。
Channel Capacity:信道容量

## Slide 20
    Where S － average transmitted power（W）
    N－ noise power（W）
    B－channel bandwidth（Hz）
    Suppose single power spectral density is n0，N = n0B.
    The channel capacity can be rewritten as：
    From the above equation, the capacity of a continuous channel depends on
    three factors: channel bandwidth B, signal power S, and noise’s PSD no.
Channel capacity——香农定理
For a continuous additive white Gaussian noise (AWGN) channel, the channel capacity is:
三要素

## Slide 21
Notes: 香农公式给出了通信系统所能达到的极限信息传输速率，但是，香农公式只证明了理想通信系统的“存在性”，却没有指出这种通信系统的实现方法。

## Slide 22
Figure The relation between C and B
S/n0
S/n0
B
Ct
1.44(S/n0)
Notes: 香农公式给出了通信系统所能达到的极限信息传输速率，但是，香农公式只证明了理想通信系统的“存在性”，却没有指出这种通信系统的实现方法。

## Slide 23
Example
Conclusion:B and S/N can be traded off.
带宽和信噪比可以互换
Reduce the requirement on SNR
Notes: 香农公式给出了通信系统所能达到的极限信息传输速率，但是，香农公式只证明了理想通信系统的“存在性”，却没有指出这种通信系统的实现方法。

## Slide 24
3.4 Channel capacity——Examples

## Slide 25
3.4 Channel capacity——Examples

## Slide 26
3 (25年期末) A geosynchronous satellite同步卫星 communication link has a carrier frequency of 14 GHz, the system bandwidth is 36 MHz between the transmitter and the receiver, and a signal to-noise ratio (SNR) of 30dB at the receiver.① Calculate the channel capacity.
(提示: The SNR in dB must first be converted to a linear value.)
②If the satellite communication link is affected by space rain attenuation, resulting in the receiver SNR dropping to 10dB while the bandwidth remains unchanged, how will the channel capacity change, calculate it.

## Slide 27
③What intuitive impact(影响) does this change have on the service bearing capacity(服务承载能力) of satellite communication (e.g., high-definition video transmission高清视频传输, large data backhaul大数据回传)? 即简单讨论对通信服务质量的影响。

## Slide 28
Definition
Discrete Channel Capacity 离散信道容量
Continous Channel Capacity 连续信道容量
Examples
Extension 扩展
Channel Capacity:信道容量

## Slide 29: Extension 拓展——example

## Slide 30
Higher-order modulation gets closer to channel capacity.
Higher-order modulation brings higher BER, and good channel coding is needed to improve the reliability of the communication system.
高阶调制误码率更高，需要优良的信道编码来提升通信系统的可靠性。

## Slide 31
Modulation: improves communication effectiveness (faster transmission, higher spectral efficiency)
Channel coding: guarantees communication reliability (accurate transmission, lower bit error rate)
调制：提升通信有效性（传得快，频谱效率）
信道编码：保障通信可靠性（传得准，降低误码）

## Slide 32: Extension 拓展：MIMO communication
Transmitter
Receiver
MIMO Communication System
. . .
. . .
MIMO multiplexing复用: multiple antennas send different information to multiply data rate.多天线传输相互独立的信息，信息传输速率可以成倍提升。
MIMO diversity 分集: multiple antennas send the same information to enhance system reliability.多天线发送相同信息，增强系统可靠性。

## Slide 33: Extension 拓展：MIMO communication
Transmitter
Receiver
MIMO Communication System
. . .
. . .
The standard channel capacity formula for MIMO:

## Slide 34
The standard channel capacity formula for MIMO:
det:determinant 行列式

## Slide 35
The standard channel capacity formula for MIMO:
Approximate MIMO Capacity Formula
(High SNR & Rich Scattering)
Special Case: 2×2 MIMO

## Slide 36
Approximate MIMO Capacity Formula
(High SNR & Rich Scattering)
Link | Antenna Config | min(Nt, Nr) | Channel Capacity
Downlink | 4×2 MIMO (BS 4Tx, UE 2Rx) |  | 
Uplink | 1×4 (UE 1Tx, BS 4Rx) |  | 

## Slide 37
3.2 A voice-grade channel of the telephone network has a bandwidth of 3.4kHz.
(a)Calculate the information capacity of the telephone channel for a signal-to-noise ratio of 30dB
(b) Calculate the minimum SNR required to support information transmission through the telephone channel at the rate of 9600bps
作业

## Slide 38: Mind map

## Slide 40
第一章 习 题 + 思维导图 + Brief summary(精练）
第二章 作业清单
+ 思维导图（2人讨论完成，互签）可打印可手写
+ Brief summary（精炼）手写
第三章 作业清单+思维导图+summary
双节大礼包