## Slide 1: Principles of communications Chapter 3 Channel—Part I

## Slide 2
Chapter 3: Channel — Part I
3.1 The classification of channels 信道的分类
--Wireless channels 无线信道
--Wire channel 有线信道
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
--Coding channel model（编码信道模型）
3.3 Influence of the channel characteristics on transmission (for modulation model)信道特性对传输的影响
3.4 Channel capacity (continuous channel) 信道容量

## Slide 3
We may classify communication channels in different ways:
Wired channel：有线信道
Wireless channel：无线信道
Transmitted media
Constant parameter channel
Random parameter channel
Channel
characteristic
恒参信道
随参信道
3.1 The classification of channels 信道的分类

## Slide 4
Wired channel：有线信道
Wireless channel：无线信道
Transmitted media
3.1 The classification of channels 信道的分类
Wired channel: guided propagation --symmetrical cable: （对称电缆） --coaxial cable（同轴电缆） --optical fiber （光纤）
Wireless channel: based on free propagation --ground wave --sky wave --LOS (line of sight) 视距

## Slide 5
Wired channel: guided propagation
--symmetrical cable: twist wire
--coaxial cable（同轴电缆）
--optical fiber （光纤）
电信号
光信号
3.1 The classification of channels 信道的分类
天才简史：高锟（光纤之父）
前香港中文大学校长高锟和George A. Hockham首先提出光纤可以用于通讯传输的设想，高锟因此获得2009年诺贝尔物理学奖。

## Slide 6
Wired channel: based on guided propagation - symmetrical cable -coaxial cable -optical fiber
Wireless channel: based on free propagation -ground wave -sky wave -LOS (Line of Sight)
3.1 The classification of channels

## Slide 7
Wireless channel: based on free propagation
--ground wave
--sky wave
--LOS (Line of Sight)
< 2MHz
2~30MHz
10000km
>30MHz
Over hundreds to
thousands of km
短波电台

## Slide 8: Summary
Wired Channel（有线信道）
① Twisted-pair cable：Low cost, used for short-range LAN. Vulnerable to electromagnetic crosstalk.
成本低，短距离局域网（网线），易受干扰。
② Coaxial cable：Better anti-interference performance than twisted pair; used in old CATV and surveillance systems.
抗干扰优于双绞线，早期有线电视、监控。
③ Optical fiber：Excellent anti-interference, huge bandwidth, long transmission distance. Used for backbone & long-haul communication.
抗干扰极强、带宽大、远距离，骨干网、长途通信。

## Slide 9: Summary
Wireless Channel（无线信道）
① Ground wave：Propagates along the Earth’s surface. Suitable for long-distance medium & long wave; capable of diffracting around surface obstacles.
沿地球表面传播，适合长距离、中长波，可绕过地表障碍物。
② Sky wave：Reflected by the ionosphere. Uses short waves for long-distance, intercontinental communication.
利用电离层反射传播，短波，可实现远距离、跨大洲通信。
③ Line-of-Sight (LOS) propagation：Microwave travels in straight line with no obstruction between two points. Applications: base stations, satellites, wireless bridges.
视线传播：微波，两点之间无遮挡，直线传输（基站、卫星、无线网桥）。

## Slide 10: Matching Question
Channels
symmetrical cable
coaxial cable
optical fiber
ground wave
sky wave
LOS (line of sight)
Applications
Long-distance high-speed backbone transmission
B. Home telephone and short-
distance LAN
C. Cable television (CATV)
D. Microwave relay, point-to-point
LOS transmission
E. Medium wave radio broadcasting
F. Shortwave over-the-horizon long-
distance radio

## Slide 11: Example 1
Assume a wireless link uses line-of-sight propagation for communication, and the heights of the transmitting antenna and the receiving antenna are both 80m.Find the maximum communication distance.

## Slide 12: Example 2
理想自由空间传播衰落模型(Friis方程)

## Slide 13
62GHz
23GHz
120GHz
180GHz
350GHz
Attenuation characteristics of the atmosphere
Wireless channel: based on free propagation

## Slide 14
Chapter 3: Channel — Part I
3.1 The classification of channels 信道的分类
--Wireless channels 无线信道
--Wire channel 有线信道
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
--Coding channel model（编码信道模型）
3.3 Influence of the channel characteristics on transmission
信道特性对传输的影响
3.4 Channel capacity (continuous channel) 信道容量

## Slide 15
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
--Coding channel model（编码信道模型）
Channel encoder
Channel decoder
Source encoder
Source decoder
Modulator
Demodulator
channel
Source of information
User of information
Encryption
Decryption
Noise
Modulation channel
Coding channel

## Slide 16
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
--Coding channel model（编码信道模型）
Channel encoder
Channel decoder
Source encoder
Source decoder
Modulator
Demodulator
channel
Source of information
User of information
Encryption
Decryption
Noise
Modulation channel
Coding channel

## Slide 17
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
--Coding channel model（编码信道模型）
Channel encoder
Channel decoder
Source encoder
Source decoder
Modulator
Demodulator
channel
Source of information
User of information
Encryption
Decryption
Noise
Modulation channel
Coding channel

## Slide 18
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
--Coding channel model（编码信道模型）
The modulation channel is a real physical channel,
while the coding channel is merely an abstract model with statistical properties.
调制信道是真实物理信道，而编码信道仅仅是具有统计特性的抽象模型

## Slide 19
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）

## Slide 20
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
Constant parameter channels（恒参信道）
Wire line（有线电话线）
Coaxial cable（同轴电缆）
Optical fiber（光纤）
Microwave line-of-sight（视距微波）
Random parameter channels（随参信道）
Shortwave ionospheric channel（短波电离层）
Mobile radio channel（移动通信无线信道）
Troposcatter channel（对流层散射信道）

## Slide 21
3.2 Channel models 信道模型
--Coding channel model
Binary coding channel model — Memoryless model
P(1 / 0)
P(0 / 1)
0
0
1
1
P(0 / 0)
P(1 / 1)
Transmitter
Receiver
转移概率

## Slide 22
P(1 / 0)
P(0 / 1)
0
0
1
1
P(0 / 0)
P(1 / 1)
Transmitter
Receiver
Example 3

## Slide 24
0
1
2
3
3
2
1
0
Receiver
Transmitter
Transition probability
X
Y
3.2 Channel models 信道模型
--Coding channel model（编码信道模型）
Quaternary coding channel model

## Slide 25: Example
( ) 1. The modulation channel is located between the output of the modulator and the input of the demodulator.
( )2. The coding channel mainly analyzes waveform distortion and amplitude-frequency distortion of analog signals.
( ) 3. The performance of the coding channel depends on the noise and distortion from the modulation channel.
What is the difference between modulation channel and coding channel?

## Slide 26
Chapter 3: Channel — Part I
3.1 The classification of channels 信道的分类
--Wireless channels 无线信道
--Wire channel 有线信道
3.2 Channel models 信道模型
--Modulation channel model（调制解调模型）
--Coding channel model（编码信道模型）
3.3 Influence of the channel characteristics on transmission
信道特性对传输的影响
--Influence of Constant parameter channels on transmission
--Influence of Random parameter channels on transmissio

## Slide 27
3.3 Influence of the channel characteristics on transmission
Ideal constant parameter channel transmission characteristics
Or Group delay（群延时）:
Amplitude-frequency characteristic：
Phase-frequency characteristic：

## Slide 28
3.3 Influence of the channel characteristics on transmission
Ideal constant parameter channel transmission characteristics
  If the input signal is s(t), then output is:
—— This case is called distortionless transmission.
无失真传输
constant attenuation
constant time delay

## Slide 29
Insertion loss插入损耗
Typical telephone channel:
In practice
Decrease of SNR and increase ISI ( Inter-symbol interference)
3.3 Influence of the channel characteristics on transmission
Practical constant parameter channel are not ideal
Linear compensation network
线性补偿网络

## Slide 30
3.3 Influence of the channel characteristics on transmission
Practical constant parameter channel are not ideal
Example: The equivalent model of a constant parameter channel is shown in the following Figure. Analyze what kinds of distortion will occur when the signal transmits through this channel.

## Slide 31
3.3 Influence of the channel characteristics on transmission
Practical constant parameter channel are not ideal
Solution The transfer function of this channel is:

## Slide 32
Most wireless channels belong to random parameter channels.
Three characteristics:
Transmission attenuation of the signal is varying with time;
Transmission delay of the signal varies with time;
Signal arrives at the receiver over several paths, i.e. multi-path propagation(多径传播)phenomenon exists.
3.3 Influence of the channel characteristics on transmission
--Influence of Random parameter channels on transmission

## Slide 33: Influence of Random parameter channels on transmission --Multipath effect(多径效应): The effect of multipath propagation on signals.
Figure. 3.3.3 Model of a multipath channel.
Constant amplitude
&single frequency
?

## Slide 34
    The receiving signal is
Influence of Random parameter channels on transmission --Multipath effect(多径效应):

## Slide 35
    The receiving signal is
    It can be written as :
Influence of Random parameter channels on transmission --Multipath effect(多径效应):

## Slide 36
Narrowband signal
    The receiving signal is
    It can be written as :
    where --- Receiving envelope
    ---Receiving phase
缓慢随机变化
缓慢随机变化
Influence of Random parameter channels on transmission --Multipath effect(多径效应):

## Slide 37
Transmitting
Receiving
Spectrum
Conclusion: When a constant amplitude single tone sine wave propagates to the receiver over n paths, the received signal can be regarded as a narrowband signal with random varying envelope and phase. Its spectrum is diffused (弥散)
waveform
Influence of Random parameter channels on transmission --Multipath effect(多径效应):

## Slide 38
Transmitting
Receiving
Spectrum
waveform
Influence of Random parameter channels on transmission --Multipath effect(多径效应):
This envelope fluctuation is called fast fading 快衰落
— the fading period is comparable to the symbol period.
i.e. fading period≈ symbol period

## Slide 39
n=2
    A f(t ➖ 0)
    A f(t ➖ 0 ➖ )
    f(t)
F()
Influence of Random parameter channels on transmission --Multipath effect(多径效应): ——简化场景： 只有两条传播路径

## Slide 40
n=2
    A f(t ➖ 0)
    A f(t ➖ 0 ➖ )
    f(t)
F()
Influence of Random parameter channels on transmission --Multipath effect(多径效应): ——简化场景： 只有两条传播路径
Discuss？

## Slide 41
Influence of Random parameter channels on transmission --Multipath effect(多径效应): ——简化场景：只有两条传播路径
Constant attenuation
Fixed time delay
欧拉公式
Since this fading depends on frequency, it is often referred to as frequency-selective fading（ 频率选择性衰落）.

## Slide 42
Influence of Random parameter channels on transmission --Multipath effect(多径效应): ——简化场景：只有两条传播路径
Constant attenuation
Fixed time delay
欧拉公式
In mobile 4G and 5G communications, this frequency-selective fading has a great impact on signals and degrades communication quality. So we need ways to solve this problem.

## Slide 43
Condition for frequency‑selective fading

## Slide 44: Example